## Slide 1: eduroam
RADIUS background and practical session

## Slide 2: exercise: build an eduroam IdP
Using FreeRADIUS + LDAP
Largely following GÉANT’s documentation:
  https://wiki.geant.org/display/H2eduroam/freeradius-sp
  https://wiki.geant.org/display/H2eduroam/freeradius-idp
But first we need to fill in some gaps

## Slide 3: F/Ticks
Simple statistical logging format:
This shows a visitor from the University of Cape Town (REALM=wf.uct.ac.za) visiting the University of the Western Cape (VISINST=1uwc.ac.za) in South Africa (VISCOUNTRY=ZA)
CSI = Calling-Station-ID = MAC address [privacy]
F-TICKS/eduroam/1.0#REALM=wf.uct.ac.za#VISCOUNTRY=ZA#
VISINST=1uwc.ac.za#CSI=4c-fb-45-de-ad-f1#RESULT=OK#

## Slide 4: Operator-Name
Provides a way to identify the [remote] service provider
There are a number of different formats, identified by the first character
  eduroam uses the REALM type, identified by “1”
  The REALM type uses a DNS-based scope
1renu.ac.ug
1mak.ac.ug
1uwm.edu

## Slide 5: Chargeable-User-Identity
A pseudo-anonymous, opaque, persistent, targeted, privacy-preserving identifier
Chargeable-User-Identity := 2a8cd315aec15e3bc3f5a3820f4466a7c4653bb8
SHA1 hash of a secret salt, User-Name, and Operator-Name
  (see policy.d/cui line 72)

## Slide 6: FreeRADIUS & virtual servers
FreeRADIUS supports virtual hosts/servers, in much the same way as Apache does
Selected based on client, port, or explicitly in config
This can be used to simplify the processing of outer and inner identifiers

## Slide 7: Federation-level RADIUS servers
For Uganda/RENU
IPs:
  eduroam-proxy.renu.ac.ug (196.43.185.12)
  radius.ucu.ac.ug (196.43.140.135)
Shared secret:
  negotiated with RENU
Realm:
  your DNS domain
For this exercise
IPs:
  137.63.190.7
Shared secret:
  9999
Realm:
  instX.fim.renu.ac.ug

## Slide 8: EAP Types
EAP type
PEAP
TTLS
GTC
TLS
MD5
SIM
Phase 2
MSCHAPv2
PAP

## Slide 9: LDAP Modules
FreeRADIUS supports LDAP, but you need to enable the module by symlinking mods-available/ldap -> mods-enabled/ldap
For the exercise, you need to configure it to talk to OpenLDAP on your own VM
In a real situation, could be your Active Directory, eDirectory, etc
NB! What LDAP backend you use affects what EAP types you can use!